##### G-4400 MODEL

"SERVICE STATION STYLE" GARAGE DOOR

Door thickness 1 3/4" (44.5 mm)

GARAGA INC.								SECTION: 08 36 13

FILE:___________________						Page:_______________

OVERHEAD RETRACTABLE DOORS

WITH METAL SECTIONS ON HINGES

PART 1: OVERVIEW

1.1	RELATED WORK

The author shall give all the necessary references.

1.1.1	Electrical connections, water tightness of openings, and so on.  Remember: all electrical connections and installations must be done by a qualified electrician as recommended by the manufacturer of the electric garage door operators.  (Section 16100)

1.1.2	Preparation of the opening of the garage door (Section 05500).

1.1.3	These construction specifications and shop drawings are applicable to Garaga Inc. products only.

1.2	SHOP DRAWINGS

1.2.1	Submit the shop drawings as per the instructions outlined in Section 01300.

1.2.2	The shop drawings shall include all the following information: the type of materials, the type of opening mechanism, the required tolerances, the electrical connections, the structural fastenings executed by the general contractor, and the suitable matching with neighboring materials.

1.3	MAINTENANCE RECORDS

1.3.1	Provide the necessary instructions to ensure proper operation and maintenance of all the hardware components for the doors as well as the electric garage door operators, and include these instructions with the manual on use and maintenance described in Section 01300.

1.4	QUALIFICATIONS

1.4.1	The installation shall be executed by a company approved by the garage door manufacturer as an installer, using skilled installers with minimum five years documented experience.

1.4.2	The manufacturer of materials shall be fabricated by a manufacturer with a minimum five years documented experience.

PART 2: GARAGE DOORS

2.1	CALCULATION CRITERIA

2.1.1	The doors and the hardware system shall be designed to meet or exceed the industry standard for windload (Door & Access Systems Manufacturer Association).

(Note: for doors wider than18’ (5.5 m), or high wind situations, consult our engineering service).

2.1.2	The doors, the tracks, and the springs shall be designed to withstand at least __________operation cycles per year and _________total cycles over their useful life.

Note: the number of spring cycles can vary from 10,000 to 100,000 cycles. However, you must realize that you cannot get the high cycles for every size of door. If you want the best operating system, with the highest cycles possible, please specify “springs shall be designed for the maximum operation cycles”.

2.2	MATERIALS

2.2.1	Tubular aluminum extrusions are 0.06” (1.6 mm) thick (choose from: Clear Anodized, pre-painted White or Black), are in accordance with ASTM B 209 and ASTM B 209M standards, model 6063 T5, and have an additional thickness of 1/8” (3.2 mm) where hinges are to be fastened.

CHOOSE…

2.2.2a	Windows have clear, double thermo panes and a total thickness of 7/8" (22 mm).  The 1/8" (3 mm) panes are sealed in aluminum extrusions using the Intercept™ system with a 5/8” (16 mm) air space.  The windows are inserted in an expanded PVC frame and factory installed by the manufacturer.

Note: there is a vast choice of glass choices including sealed panes, clear or tinted, tempered, wired, etc. Contact our Technical department for other types of glass.

2.2.2b	Windows have triple-walled fluted polycarbonate (choose clear or bronze) and a total thickness of 5/8” (16 mm). The windows are inserted in an expanded PVC frame and factory installed by the manufacturer.

CHOOSE…

2.2.3a	Bottom door section is made of double aluminum sections made up of two 0.018” (0.48 mm) steel sheets or 0.02” (0.60 mm) aluminum sheets and a 3/4" (19 mm) sheet of plywood, in the manufacturer’s standard colors. The section is fixed to the aluminum extrusion assembly with rigid PVC moldings and brackets.

2.2.3b	Bottom door section is a double-walled section in 26-gauge, G60 galvanized steel, Garaga model G-5000, polyurethane-injected with a total thickness of 1 3/4” (45 mm).

2.3	DOORS

2.3.1	The garage doors shall be the model G-4400 as made by Garaga Inc. The sections are made up of anodized tubular extrusions fastened with self-tapping screws which have a stop notch.  The extrusions shall have a minimum diameter of 6 ¼” (159 mm) at the perimeter of the door.

2.3.2	The doors shall have the following sizes and features:

LOCATION	           SIZES		  # OF SECTIONS	                  # OF PANES

OF DOORS	        (W. by H.)		     WITH PANES		    PER SECTION

__________	___________	________________		_________________

__________	___________	________________		_________________

2.3.3	The top-to-bottom end of the aluminum extrusions shall be doubled at each end in order to obtain a minimum support of 6 ¼” (159 mm) at these places. Doors 14’ 0’’ (4.27 m) wide and over will have 1  ¾ in. (45 mm) horizontal reinforcements integrated to the aluminum extrusions.

2.4	WEATHER TIGHTNESS

2.4.1	Provide and install continuous weatherstripping at the bottom of the lower section. The weatherstripping shall be made of a U-shape aluminum extrusion as well as a semi-circular TPE (thermoplastic elastomeric) tubing.

2.4.2	Provide and install, on the exterior side of the door jambs and lintel, weatherstripping made up of an aluminum extrusion as well as a double-edged strip of arctic vinyl.

2.5	OPTIONS (to choose from)

2.5.1	Exhaust ports of 3” (76 mm) in diameter are factory installed on each door in order to place flexible hoses for evacuating exhaust gases.

PART 3: HARDWARE WITH TORSION SPRINGS

3.1	PRODUCTS

3.1.1	Tracks

The tracks are made of 12-gauge (0.1” (2.6 mm)) galvanized steel, 3” (76 mm). The horizontal track is reinforced with a steel angle of 50 x 50 mm (2” x 2”).

3.1.2	Hardware

The hinges are made of 13-gauge galvanized steel. Industrial rollers, 3” (76 mm) long with 10 ball bearings, are used.

3.1.3	Struts for large doors (if applicable)

Doors 12' 4" (3759 mm) wide or wider will come with 22-gauge galvanized steel horizontal struts, and 13-gauge double hinges at each end.

3.1.4	Type of movement

The movement of the hardware will allow for the most space possible available underneath the door when it is in the open position.

LOCATION	    	      TYPE OF MOVEMENT	 	  AVAILABLE SPACE	                OF DOORS	       					 	   (FLOOR/CEILING)

____________		     _____________________	           ______________________

____________		     _____________________	           ______________________

____________		     _____________________	           ______________________

3.1.5	Torsion-type springs

The torsion spring lifting system will consist of all the parts and accessories needed for its installation.  All doors weighing more than 1000 lb. (454 kg), hardware parts included, must be approved by a professional in installation in regards to the choice of hardware (drums, galvanized cables, springs, anchor plate, solid shaft of 1” (25 mm)).

3.2	OPTIONS (to choose from)

3.2.1	3”-long (76 mm) rollers, NBSS (for car or truck washes)

Garage door rollers for 3” (76 mm) tracks will have an NBSS head on an SAE 1020 galvanized zinc-plated steel rod.

3.2.2	3”-long (76 mm) precision rollers, machined steel (for doors weighing over 770 lb., 350 kg, or dusty locations)

Garage door rollers for 3” (76 mm) tracks will have a machined steel head. They also include a sealed 6202-2RS precision ball bearing and are mounted on steel rod.

3.2.3	Track guards, L-shaped

The vertical tracks are protected by non-galvanized, L-shaped track guards 5’ x 0.3” (1524 mm x 6.4 mm), in order to avoid accidental breaking.  Often, track guards are painted with a bright color after installation.

3.2.4	Track guards, Z-shaped

The vertical tracks are protected non-galvanized, Z-shaped track guards 5’ x 0.3” (1524 mm x 5.0 mm) in order to avoid accidental breaking.  Often, track guards are painted with a bright color after installation.

3.2.5	Chain hoist

Doors of over 10’ (3 m) high with manual operation will come equipped with a chain hoist mounted on the wall.

Note: If an electric door opener is included, this option is unnecessary. Consult specs in the next section.

3.2.6	Pull chain

Manual operation doors less than 10’ (3 m) high will come with a pull chain to assist the lowering of the door.

Note: If an electric door opener is included, this option is unnecessary. Consult specs in the next section

3.2.7	Pusher springs (to choose from)

For doors exceeding 161 ft2 (15 m2), the standard movement hardware will come with pusher springs at the end of the horizontal tracks in order to prevent the cables from falling off the drums.

3.2.8	"C" bumper springs (to choose from)

For dock doors (ex: 8’ x (8’2438 mm x 2438 mm)), the vertical lift movement hardware will come with “C” bumper springs at the end of the vertical tracks.

3.2.7	Flanged bearing

The end bearing plates will come equipped with flanged bearings for doors weighing more than 660 lb. (300 kg). Center plate (football bearings) will be included with doors of this weight.

3.2.8	Tension bridge reinforcements

Doors that are 18' 3" (5563 mm) wide and over will come equipped with tension bridge reinforcements.  They will be mounted at each end of the top section and held in the center by a support whose height is adjusted according to the width of the door.  These reinforcements must be installed according to Garaga’s exact specifications.

Note: all doors which weight exceeds 1000 lb. (454 kg), including hardware parts attached to the door, must be designed according to manufacturer’s specifications. Consult the Garaga technical service department.

PART 4:	TROLLEY-TYPE OPERATORS FOR COMMERCIAL USE

4.1	PRODUCTS

4.1.1	These are trolley-type electric operators that come equipped with a quick-release device which instantly disconnects the door from the operator to enable manual operation in the event of a power failure. The system consists of a carriage that slides between dual galvanized steel angle tracks.

Note: that 4” (100 mm) of free space is required between the highest point of the door travel and the ceiling.

4.1.2	The electric motors, control mechanisms, relays, and electrical devices of the operator shall be approved according to CSA and UL standards.

4.1.3	The electrical power supply is of ____________ volts, _______ phase(s) and 60 Hz.

LOCATION		         MODEL 		HORSEPOWER	 * TYPE OF

OF DOORS								 MOVEMENT

______________	________________	  ___________		____________

______________	________________	  ___________		____________

* Standard lift only

4.1.4	The operators come equipped with an instantly reversible motor, which has built-in thermal protection mechanism. The electrical control circuit shall be 24 volts.

4.1.5	The door shall travel at approximately7.9 to 11 in. /sec (200 to 280 mm/sec).

4.1.6	The control panel for the door operator shall be the push-button type for Up/Down/Stop control and surface mounted on the inside wall.

4.1.7	A safety mechanism with photocells shall be added to each operator in order to stop and reverse the movement of the door in the event an object cuts off the light beam.

AND / OR

An electro-pneumatic safety device with an instant reverse feature will be added to each operator.  It consists of a rubber hose concealed within the weatherstripping located at the bottom of the door, combined with the electric switches. This device makes the door stop and go back up as soon as it comes into contact with an object.

4.2	OPTIONS (to choose from)

4.2.1	The door operators identified by the numbers _____ come with a remote control system.

4.2.2	A control station with a key switch for Up/Down/Stop shall be surface mounted on the outside of the building.

4.2.3	All side latches will be equipped with an electrical interlock switch to prevent use of the electric operator when the door is locked.

PART 4:	JACKSHAFT-TYPE OPERATORS

4.1	PRODUCTS

4.1.1	The electric operators shall be the Jackshaft type and shall come equipped with a built-in chain hoist assembly and with a quick release mechanism to allow for manual operation of the door in the event of a power failure.

4.1.2	The electric motors, control mechanisms, relays, and electrical devices of the operator shall be approved according to CSA and UL standards.

4.1.3	The electrical power supply is of ____________ volts,  _______ phase(s) and 60 Hz.

LOCATION		         MODEL 		HORSEPOWER	 * TYPE OF

OF DOORS								 MOVEMENT

______________	________________	  ___________		____________

______________	________________	  ___________		____________

4.1.4	The operators shall feature a positive lock mechanical brake, an instantly reversible motor, and a thermal protection device against power surges. The electric control circuit is of 24 volts.

4.1.5	The door shall travel at a speed of 7.9 to 11 in./sec (200 to 280 mm/sec).

4.1.6	The control panel for the door operator shall be the push-button type for Up/Down/Stop control and surface mounted on the inside wall.

4.1.7	A safety mechanism with photocells shall be added to each operator in order to stop and reverse the movement of the door in the event an object cuts off the light beam.

AND / OR

An electro-pneumatic safety device with an instant reverse feature will be added to each operator.  It consists of a rubber hose concealed within the weatherstripping located at the bottom of the door, combined with the electric switches. This device makes the door stop and go back up as soon as it comes into contact with an object. It also comes with a 1.5 second delay on reverse feature which helps prevent too much bouncing on the lifting cables when the door is going back up.

4.2	OPTIONS (to choose from)

4.2.1	The door operators identified by the numbers _____ come with a remote control system.

4.2.2	A control station with a key switch for Up/Down/Stop shall be surface mounted on the outside of the building.

4.2.3	All side latches will be equipped with an electrical interlock switch to prevent use of the electric operator when the door is locked.

PART 5: INSTALLATION

5.1	Before starting, make sure that the frames and the fixtures prepared by the general contractor are square.

5.2	Install the doors and the related hardware.

5.3	Apply some touch-up paint to areas where the finish might have been damaged during the mounting.

5.4	Install the electric motors, control devices, push-button control stations, relays, and other electrical equipment needed for operating the door.

5.5	All electrical connections must be done by a certified electrician.

5.6	Adjust all movable parts in such a way as to get good weather tightness against all conditions.

5.7	Adjust the weatherstripping with the exterior jambs in such a way as to get good weather tightness against all conditions.

5.8	Make sure all of the mechanisms that have been installed work properly.

5.9	Clean doors as recommended by the manufacturer, and get rid of all leftover materials and debris 		found near the openings and the hardware.

# Text boxes

CHOOSE FROM:	- Trolley-type operators for commercial use

- Jackshaft-type operators